## Slide 1
PROJECT VELOCITY: AURORA EXPRESS
Wheel Assembly Layout Proposal
Reducing bottleneck delay in the Aurora Express wheel-mounting cell through a targeted layout change
Prepared for the Manufacturing Operations Committee

## Slide 2
DETAILED ANALYSIS
Current State: Original Layout
Four assembly stations run in sequence, each near 62 minutes per unit. All stations share one overhead crane.
Warehouse
Assembly 1
61:15
Assembly 2
62:35
Assembly 3
61:46
Assembly 4
62:10
Wheel Press
Single shared crane services all four assembly stations
Note: cycle times shown are per-station totals from the time study; the crane is a shared resource across stations.
2

## Slide 3
DETAILED ANALYSIS
Analysis: Bottleneck Identified
HIGHEST-CYCLE ELEMENT
5:24.5
minutes average
“Mount wheel to axle”
~40 seconds longer than the next-slowest of all 20 recorded elements
Depends on shared crane availability
Largest single time sink
The longest of 20 timed elements in the assembly sequence, directly setting the pace of the whole line.
Resource-constrained, not skill-constrained
Duration depends on when the shared crane is free, not on operator technique — explaining the wide time spread.
Downstream queuing effect
Every later step (locking, alignment, testing, transport) waits on this station, amplifying any delay here.
3

## Slide 4
DEVELOPING THE PROPOSAL
Reference: Types of Plant Layouts
Fixed layout
Product stays in one place — too large or heavy to move (e.g. ships, buildings). Resources travel to the product.
Process layout
Similar resources grouped by function. Suits job shops making varied products in small volumes.
Product layout
Resources arranged in the exact sequence of manufacture. Ideal for mass-producing one product — our current model.
Cellular layout
Blends process and product layouts — small teams (cells) produce a range of related products.
4

## Slide 5
DEVELOPING THE PROPOSAL
Objectives of the Proposed Layout Change
Every element of the redesign is measured against these four goals.
Reduce production time
Cut the wheel-mounting cycle time by removing crane wait and manual alignment delay.
Minimize waste
Reduce rework from misalignment and cut wasted motion between storage, staging, and mounting.
Improve worker safety
Lower manual handling of the heaviest component and reduce time spent under a suspended load.
Increase production capacity
Raise overall line throughput by relieving the single slowest, most resource-constrained station.
5

## Slide 6
DESIGN OF THE NEW LAYOUT
Proposed Layout: Dedicated Lifting Cell
Assembly 2 (wheel mounting) gains its own hoist and a pre-staging zone — removing shared-crane wait time.
Warehouse
Assembly 1
61:15
Pre-stage
0:30
Assembly 2
(dedicated hoist)
≤ 61:30
Assembly 3
61:46
Assembly 4
62:10
Dedicated hoist — no shared-crane wait
What changes and why
A pre-stage cell aligns the axle on a fixed jig before the lift begins, so the hoist is only used for the final placement.
A dedicated hoist removes the wait for the shared crane, the main source of the 23-second time spread observed in the study.
Guide pins at the mounting point reduce fine-alignment time and rework from misalignment.
6

## Slide 7
JUSTIFYING THE PROPOSAL
Justifying the Change: Cost
Initial investment
Dedicated hoist / lifting fixture procurement and installation
Pre-stage jig and guide-pin fixture fabrication
Planned line downtime during changeover
Operator training on the new mounting cell
Figures are illustrative — to be finalized with vendor quotes and the finance team.
Long-term savings & ROI
~60–90 sec
estimated cut in mounting-station cycle time per unit
Higher line throughput from relieving the single largest bottleneck
Fewer rework cycles from misalignment
Reduced risk of downtime from crane contention
ROI to be modeled against actual throughput gain once the pilot cell is measured.
7

## Slide 8
JUSTIFYING THE PROPOSAL
Minimizing Disruption to Production
1
Pilot
Install the dedicated hoist and jig at Assembly 2 only, during a scheduled maintenance window.
2
Parallel run
Run the new cell alongside the existing process; compare cycle times before full changeover.
3
Full rollout
Switch the station over completely once results are validated; retire the old shared-crane routing.
Risk-mitigation strategies
Keep the original crane routing available as a fallback during the parallel-run phase.
Schedule installation work in existing maintenance windows to avoid unplanned downtime.
Train two operators per shift on the new cell before go-live to avoid single-person dependency.
8

## Slide 9
JUSTIFYING THE PROPOSAL
Highlighting the Benefits
Quantifiable improvements
Estimated 60–90 second cut in the mounting station's cycle time
Reduced variability — targets the 23-second spread seen across trials
Higher achievable throughput for the whole assembly line
Fewer rework cycles from misaligned mounting
Qualitative benefits
Less time spent manually handling the heaviest component
Reduced operator exposure to a suspended load
Smoother handoffs into downstream stations — less waiting
A more consistent, less stressful task for the mounting-cell operator
9

## Slide 10
COMMUNICATING THE PROPOSAL
Next Steps
Documentation
A full proposal document with justification, cost breakdown, and phased implementation plan, including diagrams of the current and proposed layouts.
Stakeholder presentation
A walkthrough for the Operations Committee covering the bottleneck, the redesign, and expected impact — with data-backed answers ready for likely questions.
Thank you — questions and discussion welcome.
10